## Slide 1: EE463 Hardware Project
2025-2026 Fall
DC Motor Drive
POWERpuff Boys
Mohammad Lotfi 2419364
Arda Yungucu 2517357
Hüseyin Umut Suna 2516938

## Slide 2: Topology Selection
Single Phase Diode Rectifier + Buck Converter
Three Phase Diode Rectifier + Buck Converter

## Slide 3: The Problem with the Single Phase Rectifier
Single-Phase rectification causes deep voltage ripples (100 Hz).
To maintain stable 180V output, a huge capacitor (>2000 mikroF) is required.
Also Lab inventory only provides max 470 mikroF (High Voltage) capacitors.

## Slide 4: The Solution:
Selected: Three-Phase Rectifier.
3-Phase DC bus never drops to zero (V_min = 1.5* V_peak).
Result: The available 470 mikroF capacitor is perfectly sufficient for filtering, eliminating the need for unavailable components.

## Slide 5: Our Design:

## Slide 6: Component Selection Strategy
1. Input Stage:
Component: Industrial 3-Phase Bridge Module (35A / 1000V).
Source: External procurement.
Simplifies wiring and robustness compared to discrete diodes.
2. Power Stage (Available in Lab):
IGBT: IXGH24N60C4D1 (600V / 30A).
Diode: MUR1560G (Ultrafast, trr< 60ns).
3. Safety Upgrade:
Capacitor: 470 mikroF / 450 V (for 300V DC Bus safety margin).

## Slide 7: Control Strategy (Analog Soft Start):
Controller: TL494 CN (Analog PWM Controller)
Utilizing the DTC (Dead-Time Control) pin.
An external Capacitor charges at startup >> Duty Cycle ramps linearly from 0% to Setpoint.
Objective: Analog Controller Bonus.
Controller: TL494 CN (Analog PWM Controller)
Controller: TL494 CN (Analog PWM Controller)

## Slide 8: Simulation Results (Inrush Mitigation):
Risk Analysis (Hard Start):
  Simulation showed 120 A inrush current without soft start.
  Verdict: Immediate failure of diode and IGBT.
Solution (Soft Start):
  With Ramp Logic, peak current is limited to ~9 A.
  Result: Safe operation within the SOA (Safe Operating Area) of components.

## Slide 9: Performance Verification:
Output Stability:
  Target: 180 V Output.
  Operating Duty Cycle: D = 70% (Simulation) vs 58% (Theoretical).
  Reason for difference: Real-world voltage drops (V_IGBT = 2V, Vdiode = 1.5V) included in High-Fidelity model
Ripple Check:
  Switching Frequency: 20 kHz.
  Ripple Current: < 0.5 A
  Conclusion: Motor inductance (24.5 mH) is sufficient; no external inductor needed.

## Slide 10: ANALYTICAL CALCULATIONS
Rectifier Output Voltage:
𝑉𝑑𝑐 ≈ 1.35 × 𝑉𝐿𝐿 = 1.35 × 230 V ≈ 310.5 V

## Slide 11
A discrepancy was observed between the theoretical duty cycle (𝐷𝑖𝑑𝑒𝑎𝑙 ≈ 0.58) and the simulation value (𝐷𝑠𝑖𝑚 ≈ 0.7) required to achieve the 180 V output. This is an expected outcome of the High-Fidelity modeling and is attributed to the following real-world factors:
1. Semiconductor Voltage Drops
2. DC Link Voltage Sag To compensate for these cumulative losses and the DC link sag, the Duty Cycle must be increased from the theoretical 58% to approximately 70% (𝐷 ≈ 0.7)

## Slide 12: THERMAL CALCULATIONS
Conduction Losses: The general formula for conduction loss is approximated as:
For the IGBT (Assuming 𝑉𝐶𝐸(𝑠𝑎𝑡) ≈ 2.0 𝑉at 20 A and Duty Cycle 𝐷 ≈ 0.5):
For the Diode (Assuming 𝑉𝑓 ≈ 1.5 𝑉):
Total Conduction Loss:

## Slide 13: THERMAL CALCULATIONS
Switching Losses (Frequency Dependent)
1. IGBT Switching Loss (IXGH24N60C4D1) Using the datasheet values for Turn-On (Eon) and Turn-Off (Eoff) energy at the rated test conditions (360 V, 24 A), we scaled them to our operating point (310 V, 20 A). Scaling Factor (K): Total Switching Energy per Cycle:
Power Calculation: 2. Diode Reverse Recovery Loss (MUR1560G) Diode Loss Equation: Total Switching Loss

## Slide 14: Additional System Losses
While the IGBT and Diode are the primary concerns for the main heatsink, other components also contribute to the system’s thermal load:
- Input Rectifier (SQL3510): Approximately 15 W conduction loss.
- DC Link Capacitor (470 µF, ESR ≈ 0.2 Ω): Approximately 5 W dissipation.

## Slide 15: Junction Temperature Verification
To validate the cooling system design, we calculate the expected Junction Temperature (Tj) of the components under full load, assuming an Ambient Temperature (Ta) of 25°C and an Active Fan Cooling system with a thermal resistance of RθSA = 1.0°C/W. 1. Heatsink Temperature Rise
Heatsink Temperature:
2. IGBT Junction Temperature

## Slide 16: Junction Temperature Verification
3. Diode Junction Temperature
Conclusion The thermal analysis confirms that dissipating the total system heat (~66.5 W) requires active cooling. With the selected Aluminum Heatsink + Fan combination, the component junction temperatures stabilize at approximately 122°C. This provides a safety margin of roughly 28°C below the absolute maximum rating (150°C)